## Slide 1: Lab4：Cache Lab Implementation and Blocking
Spring 2018

## Slide 2: Outline
Memory organization Cache lab
Caching
  Different types of locality
  Cache organization
Cache lab
  Part (a) Building Cache Simulator
  Part (b) Efficient Matrix Transpose
  Blocking
Supplement

## Slide 3: Memory Hierarchy

## Slide 4: Memory Hierarchy
Registers
SRAM
DRAM
Local Secondary storage
Remote Secondary storage
We will discuss this interaction

## Slide 5: SRAM vs DRAM tradeoff
SRAM (cache)
  Faster (L1 cache: 1 CPU cycle)
  Smaller (Kilobytes (L1) or Megabytes (L2))
  More expensive and “energy-hungry”
DRAM (main memory)
  Relatively slower (hundreds of CPU cycles)
  Larger (Gigabytes)
  Cheaper

## Slide 6: Locality
Temporal locality
  Recently referenced items are likely to be referenced again in the near future
  After accessing address X in memory, save the bytes in cache for future access
Spatial locality
  Items with nearby addresses tend to be referenced close together in time
  After accessing address X, save the block of memory around X in cache for future access

## Slide 7: Memory Address
64-bit machines
Block offset: b bits
Set index: s bits
Tag Bits: Address Size – b – s

## Slide 8: Cache
A cache is a set of 2^s cache sets
A cache set is a set of E cache lines
  E is called associativity
  If E=1, it is called “direct-mapped”
Each cache line stores a block
  Each block has B = 2^b bytes
Total Capacity = S*B*E

## Slide 9: Visual Cache Terminology
E lines per set
S = 2s sets
0
1
2
B-1
tag
v
valid bit
B = 2b bytes per cache block (the data)
t bits
s bits
b bits
Address of word:
tag
set
index
block
offset
data begins at this offset

## Slide 10: General Cache Concepts
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Larger, slower, cheaper memory
viewed as partitioned into “blocks”
Data is copied in block-sized transfer units
Smaller, faster, more expensive
memory caches a subset of
the blocks
4
4
4
10
10
10
Notes: Hit: it’s in the cache
Miss: the tags don’t match

## Slide 11: General Cache Concepts: Miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 12
Block b is not in cache:
Miss!
Block b is fetched from
memory
Request: 12
12
12
12
Block b is stored in cache
Placement policy: determines where b goes
Replacement policy: determines which block gets evicted (victim)

## Slide 12: General Caching Concepts: Types of Cache Misses
Cold (compulsory) miss
  The first access to a block has to be a miss
Conflict miss
  Conflict misses occur when the level k cache is large enough, but multiple data objects all map to the same level k block
    E.g., Referencing blocks 0, 8, 0, 8, 0, 8, ... would miss every time
Capacity miss
  Occurs when the set of active cache blocks (working set) is larger than the cache

## Slide 13: Cache Lab
Part (a) Building a cache simulator
Part (b) Optimizing matrix transpose

## Slide 14: Part (a) : Cache simulator
A cache simulator is NOT a cache!
  Memory contents NOT stored
  Block offsets are NOT used – the b bits in your address don’t matter.
  Simply count hits, misses, and evictions
Your cache simulator needs to work for different s, b, E, given at run time.
Use LRU – Least Recently Used replacement policy
  Evict the least recently used block from the cache to make room for the next block.
  Queues ? Time Stamps ?

## Slide 15: Part (a) : Hints
A cache is just 2D array of cache lines:
  struct cache_line cache[S][E];
  S = 2^s, is the number of sets
  E is associativity
Each cache_line has:
  Valid bit
  Tag
  LRU counter ( only if you are not using a queue )

## Slide 16: Part (a) : getopt
getopt() automates parsing elements on the unix command line If function declaration is missing
  Typically called in a loop to retrieve arguments
  Its return value is stored in a local variable
  When getopt() returns -1, there are no more options
To use getopt, your program must include the header file unistd.h
If not running on the shark machines then you will need #include <getopt.h>.

## Slide 17: Part (a) : getopt
A switch statement is used on the local variable holding the return value from getopt()
  Each command line input case can be taken care of separately
  “optarg” is an important variable – it will point to the value of the option argument
Think about how to handle invalid inputs
For more information,
  look at man 3 getopt
  http://www.gnu.org/software/libc/manual/html_node/Getopt.html

## Slide 18: Part (a) : getopt Example
int main(int argc, char** argv){
int opt,x,y;
/* looping over arguments */
while(-1 != (opt = getopt(argc, argv, “x:y:"))){
/* determine which argument it’s processing */
switch(opt) {
case 'x':
x = atoi(optarg);
break;
case ‘y':
y = atoi(optarg);
break;
default:
printf(“wrong argument\n");
break;
}
}
}
Suppose the program executable was called “foo”. Then we would call “./foo -x 1 –y 3“ to pass the value 1 to variable x and 3 to y.

## Slide 19: Part (a) : fscanf
The fscanf() function is just like scanf() except it can specify a stream to read from (scanf always reads from stdin)
  parameters:
    A stream pointer
    format string with information on how to parse the file
    the rest are pointers to variables to store the parsed data
  You typically want to use this function in a loop. It returns -1 when it hits EOF or if the data doesn’t match the format string
For more information,
  man fscanf
  http://crasseux.com/books/ctutorial/fscanf.html
fscanf will be useful in reading lines from the trace files.
  L 10,1
  M 20,1

## Slide 20: Part (a) : fscanf example
FILE * pFile; //pointer to FILE object
pFile = fopen ("tracefile.txt",“r"); //open file for reading
char identifier;
unsigned address;
int size;
// Reading lines like " M 20,1" or "L 19,3"
while(fscanf(pFile,“ %c %x,%d”, &identifier, &address, &size)>0)
{
// Do stuff
}
fclose(pFile); //remember to close file when done

## Slide 21: Part (a) : Malloc/free
Use malloc to allocate memory on the heap
Always free what you malloc, otherwise may
get memory leak
  some_pointer_you_malloced = malloc(sizeof(int));
  Free(some_pointer_you_malloced);
Don’t free memory you didn’t allocate

## Slide 22: Part (b) Efficient Matrix Transpose
1 | 5 | 9 | 13
2 | 6 | 10 | 14
3 | 7 | 11 | 15
4 | 8 | 12 | 16
1 | 2 | 3 | 4
5 | 6 | 7 | 8
9 | 10 | 11 | 12
13 | 14 | 15 | 16
Matrix Transpose (A -> B)
Matrix A Matrix B
How do we optimize this operation using the cache?

## Slide 23: Part (b) : Efficient Matrix Transpose
Suppose Block size is 8 bytes ?
Access A[0][0] cache miss Should we handle 3 & 4
Access B[0][0] cache miss next or 5 & 6 ?
Access A[0][1] cache hit
Access B[1][0] cache miss

## Slide 24: Part (b) : Blocking
Blocking: divide matrix into sub-matrices.
Size of sub-matrix depends on cache block size, cache size, input matrix size.
Try diﬀerent sub-matrix sizes.

## Slide 25: Example: Matrix Multiplication
a
b
i
j
*
c
=
c = (double *) calloc(sizeof(double), n*n);
/* Multiply n x n matrices a and b */
void mmm(double *a, double *b, double *c, int n) {
int i, j, k;
for (i = 0; i < n; i++)
for (j = 0; j < n; j++)
for (k = 0; k < n; k++)
c[i*n + j] += a[i*n + k] * b[k*n + j];
}

## Slide 26: Cache Miss Analysis
Assume:
  Matrix elements are doubles
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
First iteration:
  n/8 + n = 9n/8 misses
  Afterwards in cache: (schematic)
*
=
n
*
=
8 wide

## Slide 27: Cache Miss Analysis
Assume:
  Matrix elements are doubles
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
Second iteration:
  Again: n/8 + n = 9n/8 misses
Total misses:
  9n/8 * n2 = (9/8) * n3
n
*
=
8 wide

## Slide 28: Blocked Matrix Multiplication
c = (double *) calloc(sizeof(double), n*n);
/* Multiply n x n matrices a and b */
void mmm(double *a, double *b, double *c, int n) {
int i, j, k;
for (i = 0; i < n; i+=B)
for (j = 0; j < n; j+=B)
for (k = 0; k < n; k+=B)
/* B x B mini matrix multiplications */
for (i1 = i; i1 < i+B; i++)
for (j1 = j; j1 < j+B; j++)
for (k1 = k; k1 < k+B; k++)
c[i1*n+j1] += a[i1*n + k1]*b[k1*n + j1];
}
a
b
i1
j1
*
c
=
c
+
Block size B x B

## Slide 29: Cache Miss Analysis
Assume:
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
  Three blocks fit into cache: 3B2 < C
First (block) iteration:
  B2/8 misses for each block
  2n/B * B2/8 = nB/4 (omitting matrix c)
  Afterwards in cache (schematic)
*
=
*
=
Block size B x B
n/B blocks

## Slide 30: Cache Miss Analysis
Assume:
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
  Three blocks fit into cache: 3B2 < C
Second (block) iteration:
  Same as first iteration
  2n/B * B2/8 = nB/4
Total misses:
  nB/4 * (n/B)2 = n3/(4B)
*
=
Block size B x B
n/B blocks

## Slide 31: Part(b) : Blocking Summary
No blocking: (9/8) * n3
Blocking: 1/(4B) * n3
Suggest largest possible block size B, but limit 3B2 < C!
Reason for dramatic difference:
  Matrix multiplication has inherent temporal locality:
    Input data: 3n2, computation 2n3
    Every array elements used O(n) times!
  But program has to be written properly

## Slide 32: Part (b) : Specs
Cache:
  You get 1 kilobytes of cache
  Directly mapped (E=1)
  Block size is 32 bytes (b=5)
  There are 32 sets (s=5)
Test Matrices:
  32 by 32
  64 by 64
  61 by 67

## Slide 33: Part (b)
Things you’ll need to know:
  Warnings are errors
  Header files
  Eviction policies in the cache

## Slide 34: Warnings are Errors
Strict compilation flags
Reasons:
  Avoid potential errors that are hard to debug
  Learn good habits from the beginning
Add “-Werror” to your compilation flags

## Slide 35: Missing Header Files
Remember to include files that we will be using functions from
If function declaration is missing
  Find corresponding header files
  Use: man <function-name>
Live example
  man 3 getopt

## Slide 36: Eviction policies of Cache
The first row of Matrix A evicts the first row of Matrix B
  Caches are memory aligned.
  Matrix A and B are stored in memory at addresses such that both the first elements align to the same place in cache!
  Diagonal elements evict each other.
Matrices are stored in memory in a row major order.
  If the entire matrix can’t fit in the cache, then after the cache is full with all the elements it can load. The next elements will evict the existing elements of the cache.
  Example:- 4x4 Matrix of integers and a 32 byte cache.
    The third row will evict the first row!

## Slide 37: 补充

## Slide 39
运行driver的跑分